## Slide 1: Electrical Components

## Slide 2: SMD Resistors
These are called “chip” resistors
Parameters
  Resistance – in ohms
  Size – how long and wide
  Tolerance – in % accuracy of the Ohms rating
  Watts – amount power they can safely dissipate

## Slide 3: SMD Capacitors
These are called “chip” caps and resistors
Parameters
  Capacitance – how much energy it holds
  Voltage – Volts it can withstand
  Polarized – yes or no
  Discharge speed
  Type
    “Ceramic” – very fast
    “Tantalum” – higher capacity

## Slide 4: Resistor and Capacitor Sizes
High wattage resistors need to be large
  We won’t need these
Large capacitance caps need to be large.
  Might need these

## Slide 5: SMD Parts We Have on Hand
0805 Caps and resistors (good choice) https://www.adafruit.com/products/441
  Additional values are available
    Resistors: http://goo.gl/q7Iv7R
    Caps: http://goo.gl/p6hLXR
  And some more in my lab.
Other resistors:
  0603: http://www.digikey.com/product-detail/en/PHG2A-KIT/PHG2A-KIT-ND/383654
  1206 (don’t have but could buy): http://www.digikey.com/product-detail/en/PHE2A-KIT/PHE2A-KIT-ND/383662
Other caps
  0402-1206 Ceramic: http://www.digikey.com/product-detail/en/C-HC01-E3-KIT/445-9003-KIT-ND/3644796
  Tantalum (various sizes: http://www.digikey.com/product-detail/en/TANTTAC001D/478-3450-ND/992232
  0402 Ceramic:http://www.digikey.com/product-detail/en/DIGI-402/709-1109-ND/1859441
LEDs
  0603: http://www.digikey.com/product-detail/en/511-8003-KIT/511-8003-KIT-ND/1777670

## Slide 6: Through-hole Parts We Have
We have these kits available. You can search for the part number on digikey to find out more
  Diodes: DIODESKITFS-ND
  Schottky diodes: 497-8006A-KIT-ND
  Caps: NHG2-KIT-ND
  Big caps: P4542-KIT-ND
  Resistors: RS112-ND

## Slide 7: Part Selection
There are many choices for electronic components
  For common parts (resistors, caps, etc.) there’s a page on the wiki that says which ones to use, if possible
For less common parts, you may have to find you own
  Look on digikey
  Look on Adafruit and sparkfun
  Google around for information about design considerations
  Pour over datasheets
  Bonus points if there’s a through-hole and surface mount version

## Slide 8: Digikey Demo
Let’s find some LEDs