## Slide 1: Preparing Schematics

## Slide 2: Schematics
We need schematics for each of the five components
They must include
  The necessary components
  The necessary connections
  Information describing which parts should be installed in the resulting board
  Information to make it easy to order those parts.

## Slide 3: Break Out Boards
For the IMU and micro controller BOBs the schematics are linked to from the wiki.
You need to modify them to make them schematics we can build
  Use parts we can acquire
  Ensure that necessary library components are present
You need to eliminate unnecessary parts
  Voltage level conversion
  Local power supply
Document the changes you made and how the resulting schematic works.

## Slide 4: New Schematics
For the motor controller, controller/transmitter, and power supply you’ll build a new schematic
It needs the same information as the BOB-based schematics

## Slide 5: Part Selection
There are many choices for electronic components
  For common parts (resistors, caps, etc.) there’s a page on the wiki that says which ones to use, if possible
For less common parts, you may have to find you own
  Look on digikey
  Look on Adafruit and sparkfun
  Google around for information about design considerations
  Pour over datasheets
  Bonus points if there’s a through-hole and surface mount version

## Slide 6: “Chip” component Sizes
High wattage resistors need to be large
  We won’t need these
Large capacitance caps need to be large.
  Might need these

## Slide 7: Schematic Tour
https://github.com/adafruit/Adafruit-LSM303-PCB
  Note for steve: research/NVSL/src/Quadcopters/Class

## Slide 8: Libraries

## Slide 9: Our Libraries
All symbols, packages, and devices must be in our communal libraries
  One common parts
    Resistors
    Caps
    Other frequently-used parts.
  Per-component libraries for each piece of the quadcopter
    They should live in Library/LBR in the git repo.
These are in Library/LBR
We keep them separate because merging changes with git is not reliable.

## Slide 10: Configure Eagle to use Our Libraries
From the control panel
Options->Directories
Add <PATH-TO-GIT>/Library/LBR to the “Libraries” field. It’s colon-separated.

## Slide 11: Third Party Libraries
There are many Eagle Libraries available
The adaftruit and sparkfun libraries are in our git repo (Libraries/LBR)
Eagle itself comes with a bunch too
Access them via the control panel

## Slide 12: Borrowing Stuff From 3rd Party Libraries
You can borrow stuff from 3rd party libraries, but you must be careful
  Double check all dimensions
  Be sure to check/set attributes correctly
  Add a “source” attribute with where you got it
When you borrow, you must copy it to the correct library for the course
  Open the library you want to copy to
  Find the item in the control panel library browser
  Right click and select “copy to library”

## Slide 13: Extracting Libraries from Schematics
Eagle schematics contain the library data for all the devices they use
You can extract this information for use in other schematics
  Open the schematic
  File->Export->Libraries
Once this is done, see the previous slide.

## Slide 14: Adding Attributes to Devices
Name and Value
  “Name” is used as the “reference designator” for the device.
  “Value” is resistance for resistors, capacitance for capacitors, etc.
  Set these in the schematic editor with the “Name” and “Value” tools
  These are set per-instance
Attributes attach key-value pairs to devices
  You can define any attribute you want using the device editor: Click on the “attributes” link in lower left of the editor window
  These are set in the library
  You can edit them on a per-instance basis with the “attribute” tool.

## Slide 15: Standard Attributes for This Class
Value
  Ohms for resistors
  Capacitance caps
  Etc.
DIST-1 – Distributer 1
DIST-1-PN – Distributer 1 part number
MFR – Manufacturer
MFR-PN – Manufacturer part number
CREATOR – who built the part originally
REVIEWER1 – who did the design review of the part
REVIEWER2 – who did the design review of the part
Others as needed

## Slide 16: Generating the Bill of Materials (BOM)
I added a section the Button and Light Tutorial for generating a BOM.
ULP – User Language Program
  Language for analyzing schematics, libraries, and boards programmatically.
  Can do some modifications, but its clunky
A ULP program generates the BOM.

## Slide 17: Design Reviews

## Slide 18: Attention to Detail
Getting a PCB to work means getting nothing wrong
We won’t have time for a respin, so we get one shot
We are sharing a lot of stuff – schematics, devices, etc.
We have to get everything right if we want to end up with a flying quad copter.
It’s called hardware for a reason.

## Slide 19: Design Review Process
Every device in our library and every schematic will be reviewed by at least two other people.
  Fill in REVIEWER1 and REVIEWER2 attributes
  If you review a part, you are just as responsible for errors as the original designer.
If you really want your quadcopter to fly, you should consider reviewing everything yourself.
Do not be afraid to call out problems.
Do not take problems that other people identify in your work personally. They are helping you.

## Slide 20: Design Review Process (Cont.)
How to get someone to do a review:
  Ask them.
  If someone asks, accept
Reviewers must be steadfast, picky, and demanding
  Remember, the design is going to end up in your hardware.
  Do not accept hand waving!
  If you are not sure, ask someone else.

## Slide 21: Design Reviews for Devices
Designing packages, symbols, and devices is a well defined task, determining whether its correct is relatively easy.
The designer should provide all the necessary materials
  Appropriate datasheets
  Preferably an example of the part you designing for.
  Any other necessary documentation.
The reviewer should do the review on their own and then meet with the designer to ask questions.
Make sure to allocate enough time for this meeting – 30 min at least.
It is not the designer task to convince the reviewer that their design is right. The reviewer must convince themselves, one way or the other.

## Slide 22: Design Review Checklist for Devices
Basics
  Did the designer give you the correct data sheet?
  Did they design for the right package?
  Is the item available on Digikey?
  Should they have used a part we stock in the lab?
Pad size and location
  Pad dimensions for surface mount parts
    Does the pad extend at least 1mm out from the side of the package, so its easy to solder?
    Does it otherwise match the manufactures recommendations?
  Hole diameter for through-hole parts.
    Bigger than the wire.
    Plating will make it smaller. Will it still be big enough?
Pin Numbers and Mapping
  Do the pins in the schematic symbol map to the right physical pins?
  Do the physical pins match what’s in the data sheet?
  Are you sure you understand how the drawings in the data sheet are oriented?
Silkscreen
  Are all the silk screen element in layer tPlace?
  Does the silk screen show how the device should be oriented?
  Does it include a bounding box? It should.
  Do lines of the silkscreen cross pads? They shouldn’t.
  Is the Name attribute in tPlace? It should be
  Is the Value attribute in tPlace? It shouldn’t be.
  Is all text in tPlace in the vector font? None of the other fonts work.
Documentation
  Is the Value attribute in tDocu? It should be.
  Is there a bounding box on the in tKeepout?
  Did they set the prefix for the device?
    Resistors, R
    Capacitors, C
    Inductors, L
    Diodes,D
    Transistors,Q
    ICs, U
    Header pins, J
    Jacks & Plugs,J
    Switches,S

## Slide 23: Design Reviews for Schematics
The requirements for each schematic are different, so the criteria for correctness are harder to define
The designer should present the design to the reviewer.
  The designer needs to present it clearly and logically -- this will require some preparation.
  Describe one piece at a time (Power supply, then IO, the status indicators, etc.)
The reviewer…
  Should have looked over the design ahead of time
  Must ask tough questions
  Must not accept vague reponses

## Slide 24: Design Review Checklist for Schematics
Documentation
  Are all the names and values visible?
  Is the schematic layed out nicely? Is it organized?
Connectivity
  Are all non-connected nets labeled?
  Are all pins on all parts connected? If not, why?
  Are all the grounds connected? Is there only one ground?
  Are all the Vdds connected? Is each power pin attached to the right power supply?
  Are all the pins actually connected? Or do they just look connected?
  Are there junctions at net crossings where there shouldn’t be? Are junctions missing where they should be present?
Functionality
  Does the schematic do what it’s supposed to?
  Why was the value of each resistors and cap chosen?
  E.g.: Can the power supply provide sufficient current?
  Is there sufficient decoupling?
  Are the decoupling caps the right size?
Have all the devices been through proper design reviews?