## Slide 1: Layers and CAM

## Slide 2: Layers
Eagle (and other board design tools) use layers to specify different types of information about a board. E.g:
  Where wires should go on each physical layer
  Where wires should not go on each physical layer
  Documentation
  Mechanical information
Eagle defines 52 layers by default
‘t’ prefix means top.
‘b’ prefix means bottom (displayed mirrored)

## Slide 3: Eagle Layers
Top | Tracks, top side |  | 27 | tValues | Component VALUE, top side |  | 
Route2 | Inner layer |  | 28 | bValues | Component VALUE, bottom side |  | 
Route3 | Inner layer |  | 29 | tStop | Solder stop mask, top side (gen. autom.) |  | Design
Route4 | Inner layer |  | 30 | bStop | Solder stop mask, bottom side (gen. Autom.) |  | Documentation
Route5 | Inner layer |  | 31 | tCream | Solder cream, top side |  | Tool guidance
Route6 | Inner layer |  | 32 | bCream | Solder cream, bottom side |  | 
Route7 | Inner layer |  | 33 | tFinish | Finish, top side |  | 
Route8 | Inner layer |  | 34 | bFinish | Finish, bottom side |  | 
Route9 | Inner layer |  | 35 | tGlue | Glue mask, top side |  | 
Route10 | Inner layer |  | 36 | bGlue | Glue mask, bottom side |  | 
Route11 | Inner layer |  | 37 | tTest | Test and adjustment information, top side |  | 
Route12 | Inner layer |  | 38 | bTest | Test and adjustment inf., bottom side |  | 
Route13 | Inner layer |  | 39 | tKeepout | Restricted areas for components, top side |  | 
Route14 | Inner layer |  | 40 | bKeepout | Restricted areas for components, bottom s. |  | 
Route15 | Inner layer |  | 41 | tRestrict | Restricted areas for copper, top side |  | 
Bottom | Tracks, bottom side |  | 42 | bRestrict | Restricted areas for copper, bottom side |  | 
Pads | Pads (through-hole) |  | 43 | vRestrict | Restricted areas for vias |  | 
Vias | Vias (through all layers) |  | 44 | Drills | Conducting through-holes |  | 
Unrouted | Airlines (rubber bands) |  | 45 | Holes | Non-conducting holes |  | 
Dimension | Board outlines (circles for holes) *) |  | 46 | Milling | Milling |  | 
tPlace | Silk screen, top side |  | 47 | Measures | Measures |  | 
bPlace | Silk screen, bottom side |  | 48 | Document | Documentation |  | 
tOrigins | Origins, top side (generated autom.) |  | 49 | Reference | Reference marks |  | 
bOrigins | Origins, bottom side (generated autom.) |  | 51 | tDocu | Detailed top screen print |  | 
tNames | Service print, top side (component NAME) |  | 52 | bDocu | Detailed bottom screen print |  | 
bNames | Service print, bottom s. (component NAME) |  |  |  |  |  | 

## Slide 4: Layer Demo

## Slide 5: Layers In Packages
Packages have layers too, but not all of them
  E.g. no inner metal layers
For packages “t” means device side, “b” means opposite side.
If you put the devices on the back side of the board, “t” and “b” will swap.

## Slide 6: CAM Layers (Gerber files)
Eagle layers are for design.
CAM layers are for manufacturing
  “Gerber” files are for lithographic steps
  Drill files are for drilling holes.
Each CAM layers corresponds to one layer of the resulting board
  Top silk screen
  Top solder mask
  Top metal
  Inner metal layers
  Bottom metal
  Bottom solder mask
  Bottom silk screen
One drill file specifying where all the pads, vias, and mounting holes are located and their diameters
Other files too, depending on the manufacturing process
  Solder paste stencil
  Assembly drawings

## Slide 7: The CAM Processor
The CAM Processor generates CAM files
The exact configuration for the gerber files varies by board house
  Should the board outline be in every layer?
  Which format should the files be in (there are many)
  Should the back side layers be mirrored?

## Slide 8: CAM Setup
To prepare Gerbers for a particular board house, you need CAM setup files (*.cam for Eagle)
This specifies how to generate each layer the board house needs.
See example in Button and Light Tutorial.

## Slide 9: CAM Demo

## Slide 10: Checking Your Gerbers!
Eagle can’t display Gerber files itself
You need a 3rd party tool
  See the Button and Light tutorial for recommendations
You should always check your Gerbers!
  Eagle has bugs (I assume)
  You may have misconfigured something
  You may have put something in the wrong layer.

## Slide 11: Gerber Viewer Demo

## Slide 12: DFM Checks
You should also run a “design for manufacturing” (DFM) check on your Gerbers, if possible
Freedfm.com will do this for you.

## Slide 13: FreeDFM Demo